## Slide 1: The Framework for Aquatic Biogeochemical Models
Jorn Bruggeman, Karsten Bolding

## Slide 2: Aquatic modelling needs flexibility: challenges
climate
carbon sequestration
deoxygenation
acidification
bioremediation
eutrophication
coastal erosion prevention
food provision
fisheries
aquaculture
Plankton Functional Types
(variable) stoichiometry
C, N, P, Si, Fe
structured populations
size vs. abundance
mammals & birds
leisure, recreation
bathing water quality
jellyfish, harmful algae
charismatic species
model ingredients
macrophytes, seagrasses
fish & fisheries
benthic fauna
carbonate chemistry
oxygen, redox chemistry
IBMs
ecology
biogeochemistry
questions
pelagic & benthic life stages

## Slide 3: Aquatic modelling needs flexibility: domains
world ocean
lagoons
estuaries
shelf seas
ocean basins
coastal ocean models
GETM, ROMS, …
global circulation models
NEMO, MOM, …
unstructured grid models
FVCOM, SCHISM, …
scale
resolution
model of choice
domain

## Slide 4: Aquatic modelling needs flexibility: analysis needs
1D water columns
box models
3D unstructured grids
3D structured grids
Markov Chain Monte Carlo
simulation
calibration
ensembles
sensitivity studies
data assimilation
grid parameter space
# runs needed
spatial detail
models
type of analysis

## Slide 5: No one size fits all – abandon tight coupling
light
salinity
phytoplankton
zooplankton
CO2
NO3-
PO42-
O2
fish
bacteria
detritus
temperature
Even if the conceptual model looks like this:
… should the code do so as well?

## Slide 6: FABM: “separation of concerns”
FABM
hydrodynamic model
memory management
advection, diffusion, time integration
input-output
provide physical quantities
density
temperature
salinity
full spatial domain
local point in space
biogeochemical models
define own variables and external dependencies (names, units)
request parameter values
given a local environment, provide local source terms, surface/bottom fluxes, vertical velocities
phytoplankton
API
API
zooplankton
API
nutrient
API
detritus
API
pressure
shortwave radiation
bottom stress
wind speed
all online coupled
FABM runs in host with same grid and domain decomposition

## Slide 7: About FABM
Developed since 2009 (EU FP7 project “MEECE”)
Aims:
  portability: share one biogeochemical code between different hydrodynamic models (0D, 1D, 2D, 3D)
  modularity: stand-alone, process-specific biogeochemical modules, combined to create the ecosystem – at run time
One library, runs in host with same grid and domain decomposition
  No coupling across grids or time steps
  No domain decomposition and parallelization
  Thus, FABM does not overlap or compete with MCT, OASIS, ESMF
Fortran 2003 (Intel, gfortran, Cray, PGI, AMD)
Code + extensive documentation: https://fabm.net
Published
  Bruggeman & Bolding (2014) A general framework for aquatic biogeochemical models. Environmental Modelling & Software 61, 249–265. 10.1016/j.envsoft.2014.04.002

## Slide 8: Development, licensing, copyright
FABM framework
  Developed by Bolding & Bruggeman
    Continuous development and maintenance (long-term BB strategic investment)
    Feature/coupler development funded by dedicated projects
  License: GNU General Public License (GPL)
Biogeochemical models
  Distributed with FABM or hosted externally (e.g. ERSEM)
  Developed and maintained by third parties
  License: GPL or more permissive (FreeBSD, LGPL, MIT, CeCILL)
Couplers for physical models
  Distributed with physical model
  Developed and maintained by third parties
  License: GPL or more permissive (FreeBSD, LGPL, MIT, CeCILL)

## Slide 9: FABM today: distributed development
hydrodynamics
box model
Python
C
R
GOTM
GLM
BROM-tp
MATLAB
GETM
MOM
FVCOM
NEMO
ROMS
ESMF
SCHISM
HYCOM
FESOM-C
HAMSOM
FABM
biogeochemistry
MEDUSA
BSEM
ECOSMO
ERGOM
AED
PCLake
MAECS
BROM-bio
DEB
seagrass
mizer (fish)
spectral irradiance
SELMA
ERSEM
suspended sediment
ShellSIM
3D
1D
0D
scripts
BFM
PISCES
ecosystem
models
process
models

## Slide 10: FABM today: distributed development
FABM is a core component of:
Copernicus Marine Service: North-West European Shelf (NEMO + ERSEM) & Arctic (HYCOM + ECOSMO)
EU Joint Research Centre policy evaluation suite (GETM + ERSEM/ERGOM/BSEM)
Additional CMEMS biogeochemical models (BFM, PISCES) implemented in H2020 SEAMLESS

## Slide 11: Distributed development: where is the code?
FABM
framework
third-party BGC models
(src/models)
ERSEM
updated by owner via Pull Requests
external BGC models
PISCES
BFM
Often on GitHub
Almost always open source
Updated as needed by owners
On GitHub
open source: GPL v2
ShellSIM
spectral light
…
Combined at compile time
No changes to FABM needed
external hydrodynamic couplers
NEMO
ROMS
FVCOM
FESOM
SCHISM
…
Distributed as part of physical model, or as fork

## Slide 12: What does FABM actually do? 1. Define communication between physics and BGC
BGC
initialize
do
do_bottom
do_surface
get_vertical_movement
get_light
FABM
get_parameter
register_state_variable
register_diagnostic_variable
register_dependency
add_to_aggregate_variable
It’s a contract
designed to remain stable
backward compatibility is preserved when possible

## Slide 13: What does FABM actually do? 2. Call ordering based on dependencies
light absorption [interior]
zenith angle [surface]
light [column]
phytoplankton [interior]
(but reality is more complex – ERSEM has 100s of interlinked calls)

## Slide 14: What does FABM actually do? 3. Pack/unpack data
biogeochemical models
1D, no mask
FABM
cache
read
write
Host
3D + mask
all
operations
API call
selected region
var1
var2
var3
pack data
unpack data
var1
var2
var3
out1
out2
out3
out4
out5
API result
out1
out2
out3
out4
out5

## Slide 15: Design: conceptual domain
interior
surface
bottom
state (# m-2)
ice algae
atmosphere
diagnostics
air-sea flux of CO2
state (# m-3)
nutrients
plankton
suspended sediment
diagnostics
primary production
pH
photosynthetically active radiation
state (# m-2)
bed sediment
benthic fauna
pore water nutrients
diagnostics
erosion flux

## Slide 16: Design: conceptual domain
API: do_surface
sources of surface state variables (# m-2 s-1)
surface flux of interior state variables (# m-2 s-1)
surface diagnostics
API: do
sources of interior state variables (# m-3 s-1)
interior diagnostics
API: get_vertical_movement
residual vertical velocity of interior state variables (m s-1)
API: do_bottom
sources of bottom state variables (# m-2 s-1)
bottom flux of interior state variables (# m-2 s-1)
bottom diagnostics
interior
surface
bottom

## Slide 17: ERSEM: an example of modular modelling
Inception: early 1990s
Applications
carbon and nutrient budgets
projecting ecosystem change
fish, fisheries & aquaculture
biodiversity
carbon capture and storage
ocean acidification
invasive species/harmful algae
habitat definition
>200 peer-reviewed papers
PML: 18 people developing
biogeochemical processes
ecosystem structure
programming infrastructure
Butenschön et al 2015 GMD

## Slide 18: ERSEM: an example of modular modelling
passive particle
options: sinking and remineralisation
primary producer
options: silicate use, calcification
predator with variable stoichiometry
user-specified selection of prey, overwintering behaviour
predator with fixed stoichiometry
user-specified selection of prey
calcium carbonate
dissolution dependent on saturation state
oxygen
exchange with atmosphere over water surface
carbonate system
exchange with atmosphere over water surface, pH
bacteria
user-specified selection of substrates
ERSEM =
6 x
1 x
1 x
1 x
4 x
1 x
2 x
1 x

## Slide 19: ERSEM: an example of modular modelling
Each module can appear any number of times
Mix-and-match: any model component can be replaced by observed data
What makes it unique?
Configure everything by editing one text file – no code, programming, compilation
The same configuration and code everywhere: 0D, 1D (ERSEM workshops), 3D

## Slide 20: Coupling: combining stand-alone modules
mesozooplankton
prey 1
prey 1
prey 1
C
Fe
Si
P
N
C
temperature
diatoms
Chl
phosphate
phosphate
P
temperature
hydrodynamic model
salinity
temperature
medium POM
Fe
Si
P
N
C
Fe
Si
P
N
C
detritus
Fe
Si
P
N
C

## Slide 21: Modular ERSEM – benefits
Tailor model complexity to application
  Reduce complexity where required: computational cost of high-resolution hydrodynamics does not allow many (>25) biogeochemical state variables in Earth System Models
  Increase complexity where needed: questions on biodiversity, invasive species demand the capability to freely add/remove groups
Tailor feature set to application
  Different questions, different features: carbonate system, redox chemistry, size-structured higher trophic levels, fisheries, seagrass
  Flexible currencies: biogeochemical cycles need C, N, P, Si, Fe; end-to-end food webs need abundance and size
Collaborate
  Import: redox chemistry, size-structured fish community
  Export: carbonate system

## Slide 22: Modular ERSEM – what have we gained?

## Slide 23: A wealth of component models
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
sediments
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Note: FABM makes coupling between biogeochemical component models easier, but that does not mean everything is “plug and play”
Compatibility between component models often requires that they use a similar level of detail – e.g., they describe the same elemental cycles

## Slide 24: FABM: a biogeochemical modeller’s perspective
Enable distributed development
  different people/institutes writing process-specific modules that remain compatible
  mix in 3rd party modules: ERSEM carbonate chemistry, benthic fauna, NIVA redox chemistry
Code once, run anywhere
  test in 0D (scripting languages!) and 1D before 3D simulation
  share modules across domains: use the same microbial processes and chemistry in ice, water, sediment
Stay flexible with “lego brick biogeochemistry”
  allow questions and constraints to dictate final ecosystem complexity

## Slide 25: FABM: a user’s perspective
zooplankton
concentration
mortality sink
excretion sink
detritus
concentration
phytoplankton
concentration
mortality sink
excretion sink
mineralization sink
prey
nutrient
nutrient
concentration
instances:
nutrient:
model: examples/npzd/nut
initialization:
c: 1.0
phytoplankton:
model: examples/npzd/phy
initialization:
c: 0.001
coupling:
nutrient_source: nutrient/c
excretion_sink: nutrient/c
mortality_sink: detritus/c
zooplankton:
model: examples/npzd/zoo
initialization:
c: 0.001
coupling:
prey_source: phytoplankton/c
excretion_sink: nutrient/c
mortality_sink: detritus/c
detritus:
model: examples/npzd/det
initialization:
c: 0.0
coupling:
mineralization_sink: nutrient/c
fabm.yaml

## Slide 26: FABM: a user’s perspective
Run-time configurability
  Specify ecosystem structure at run-time; no programming, preprocessing or compilation needed
Why?
  Empower end users: give maximum control, but shield from programming mistakes
How?
  Single configuration file in YAML format (http://yaml.org)
Cost?
  Negligible: work >> overhead of run time coupling and communication
instances:
nutrient:
model: examples/npzd/nut
initialization:
c: 1.0
phytoplankton:
model: examples/npzd/phy
initialization:
c: 0.001
coupling:
nutrient_source: nutrient/c
excretion_sink: nutrient/c
mortality_sink: detritus/c
zooplankton:
model: examples/npzd/zoo
initialization:
c: 0.001
coupling:
prey_source: phytoplankton/c
excretion_sink: nutrient/c
mortality_sink: detritus/c
detritus:
model: examples/npzd/det
initialization:
c: 0.0
coupling:
mineralization_sink: nutrient/c
fabm.yaml

## Slide 27: FABM: a physical modeller’s perspective
Access a vast biogeochemical library by coupling once
  enumerate state variables, diagnostic variables, conserved quantities
  access source/sink terms, boundary fluxes, vertical movement, …
Seamless integration: FABM adapts to host by taking
  number of dimensions (0-3)
  index of vertical dimension
  index of dimension to vectorize
  mask data type, masked value, mask domain (full or hz-only)
and defines its interfaces as a result:
Compiled as a library, no dependencies
fabm_do()
fabm_do(kstart,kstop)
fabm_do(istart,istop,j,k)
fabm_do_surface()
fabm_do_surface()
fabm_do_surface(istart,istop,j)
0D:
1D:
3D:

## Slide 28: Performance example (FVCOM)
Chart: run time relative to physics-only
| passive | Fasham | ERGOM | ERSEM
physics | 1 | 1 | 1 | 1
advection (ADV) | 0.1373 | 0.96722 | 1.3319 | 6.8231
advection smoother (FCT) | 0.0055392 | 0.053378 | 0.074204 | 0.37802
vertical diffusion (VDIF) | 0.0048321 | 0.018826 | 0.025904 | 0.12332
open boundaries (BCOND) | 0 | 0 | 0 | 0.0013405
vertical movement (sinking/floating) | 0.0037714 | 0.031229 | 0.050729 | 0.63807
sources | 0.015439 | 0.065116 | 0.097949 | 1.8472
range checks | 0.010018 | 0.065781 | 0.099568 | 2.1823
conservation checks | 0.0015321 | 0.012182 | 0.01592 | 0.39946
BGC
FABM
 | pelagic state variables | benthic state variables
passive | 1 | 0
Fasham | 7 | 0
ERGOM | 10 | 2
ERSEM | 50 | 36
Profiling: Intel Fortran compiler 14.0, LIMITED_2;GCY1;MPDATA;FABM;WET_DRY;MULTIPROCESSOR;PROJ, serial run

## Slide 30: Component models - ERSEM
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Butenschön et al. 2016 GMD

## Slide 31: Component models - ERSEM
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Each module can appear any number of times
Mix-and-match: any model component can be replaced by observed data
What makes it unique?
Configure everything by editing one text file – no code, programming, compilation
The same configuration and code everywhere: 0D, 1D, 3D
ERSEM: a showcase for modular ecosystem modelling
Butenschön et al. 2016 GMD

## Slide 32: Component models - fish
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
sediments
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Applications:
fish stocks/fisheries
aquaculture
improving top closure
Model:
size-based (1 mg – 100 kg, 100 classes)
pelagic feeding only
depth-integrated
different fisheries parameterizations
Blanchard et al. 2014 J Appl Ecol

## Slide 33: Component models - fish
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
sediments
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Powley et al. in prep
g WM/m2/d
#/g WM
fish biomass
fish reproduction
Helen Powley
hpo@pml.ac.uk

## Slide 34: Component models - ShellSIM
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Hawkins et al. 2013 J Shellfish Res

## Slide 35: Application – mussel farms
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Rope-cultured blue mussels, Lyme Bay, Devon, UK
Expanding: 3 sites, > 10,000 ton/year
  environmental impacts
  HABs
  river pathogens
  food web resources
Modelling: FVCOM + ERSEM + ShellSIM
Ricardo Torres
rito@pml.ac.uk

## Slide 36: Application – mussel farms
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
mussel production
increased POC flux at bed
increase in benthic fauna
decrease in pore water oxygen
Ricardo Torres
rito@pml.ac.uk

## Slide 37: Component models - seagrass
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Baird et al 2016 Ecol Mod
Applications:
coastal carbon budgets
erosion/coastal defence
eutrophication indicators
Matthew Adams
m.adams5@uq.edu.au

## Slide 38: Application – seaweed/seagrass distribution changes
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Zostera
Posidonia
Cystoseira
Saccharina
Laminaria

## Slide 39: Application – seaweed/seagrass distribution changes
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
machine learning
Start: artificial neural networks [Python] used previously to predict e.g. river flow/concentration
process-based model in Python-FABM
Start: seagrass model (Baird et al. 2016)
To be generalized to seaweeds (e.g., allow nutrient uptake by above-ground biomass)
temperature response, light capture, nutrient uptake
potential
biomass
annual mean
production
annual mean
respiration
wave
exposure
salinity
…
biomass

## Slide 40: Component models – spectrally resolved irradiance
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
sediments
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
3D ocean interior – for every single layer
absorption & scattering by Inherent Optical Properties
ocean surface
reflection & refraction
phytoplankton
detritus
dissolved organics
lower atmosphere
scattering and absorption – Rayleigh, aerosols, clouds
upper atmosphere
absorption by water vapour, ozone, oxygen, carbon dioxide
seawater
underwater PAR
total scattering: b(λ)
total absorption: a(λ)
photosynthesis
heating
Applications:
photodegradation (UV)
assimilation of satellite data (water leaving irradiance)
Gregg & Rousseaux 2016 Front Mar Sci

## Slide 41: Component models – spectrally resolved irradiance
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
sediments
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Gregg & Rousseaux 2016 Front Mar Sci
Feedback from light (FABM) to NEMO temperature improves bloom timing:
Jozef Skákala
jos@pml.ac.uk

## Slide 42: Application – sea lice treatment in fish farms
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Salmon farms, Hardangerfjord & Øygarden, Norway
Sea lice treatments in fish cages are potentially harmful to pelagic and benthic ecosystems
Environmental impact assessments track the fate of treatment agents. But these are transported in non-standard ways!
Some adsorb to particulate organics [fish waste]
Some affect water density (feedback to physics)

## Slide 43: Application – sea lice treatment in fish farms
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Hydrogen peroxide is denser than water, and the mixture used for de-licing will be ~2 ‰ denser than surrounding water. In a homogeneous water column it will sink to 100 m in ~ 7 - 8 minutes.
The simulation of a sinking plume of hydrogen peroxide shown here is created with non-hydrostatic FVCOM.
Ole Anders Nøst
ole.anders.nost@akvaplan.niva.no

## Slide 44: Application – sea lice treatment in fish farms
plankton
ERSEM
MEDUSA
higher trophic levels
spectral light
ingredient X
seagrass
fish - MIZER
bivalves - ShellSIM
carbonate chemistry
Dynamic Energy Budgets
Ole Anders Nøst
ole.anders.nost@akvaplan.niva.no
Simulation of a single release from Sauøyna